How to Program in Assembly Language
for the
Lesson 12: Tiles

---
VERA Registers
- I/O Address Space: $9F20-9F3F (32 bytes)
- Only way for CPU program to control and access VERA
- Two 8-bit data channels to 17-bit VRAM address space (128 kB)
- 8-bit data channel to 4 kB PCM FIFO (write only)
- 8-bit data channel to SPI controller

---
VRAM Interface
- CTRL: $9F25
  - Set address port (ADDRSEL) in bit 0
- ADDRx_H: $9F22
  - Set bit 16 of VRAM address in bit 0
- ADDRx_M (VRAM address bits 15:8): $9F21
- ADDRx_L (VRAM address bits 7:0): $9F20
- DATA0 (read or write byte from address 0): $9F23
- DATA1 (read or write byte from address 1): $9F24
Reset (W/O)	-	-	-	-	-	DCSEL	ADDRSEL
Address Increment (Stride)	DECR	-	-	ADDR(16)

---
Writing Array to Even Addresses
Copy array bytes to even bytes in VRAM starting at $00000
VERA_addr_low = $9F20 lda #>VRAM_DEST
VERA_addr_high = $9F21 sta VERA_addr_high
VERA_addr_bank = $9F22 lda #<VRAM_DEST
VERA_data0 = $9F23 sta VERA_addr_low
VERA_ctrl = $9F25 ldx #0
VRAM_DEST = $00000 @loop:
array: .byte 8,5,12,12,15 lda array,x
start: sta VERA_data0
   stz VERA_ctrl inx
   lda #($20 | ^VRAM_DEST) cpx #(start-array)
   sta VERA_addr_bank bne @loop

---
VERA Graphics Configuration
- DC_VIDEO: $9F29
  - Default: $21 (Layer1 Enable, Output Mode = Standard VGA)
- DC_HSCALE: $9F2A
  - Default: 128 (640 pixels wide)
- DC_VSCALE: $9F2B
  - Default: 128 (480 pixels high)
- L0_CONFIG: $9F2D; L1_CONFIG: $9F34
  - Layer 1 Default: $60 (128x64 16-Color Text)
- L0_MAPBASE: $9F2E; L1_MAPBASE: $9F35
  - Layer 1 Default: $00 (Tile map starts at $00000 = $00 << 9)
- L0_TILEBASE: $9F2F; L1_TILEBASE: $9F36
  - Layer 1 Default: $7C (8x8 tiles start at $0F800 = $7C << 9)
Current Field	Sprites Enable	Layer1 Enable	Layer0 Enable	-	Chroma Disable	Output Mode
Map Height	Map Width	T256	Bitmap Mode	Color Depth
Tile Base Address (16:11)	Tile Height	Tile Width

---
Layer 1 Tilemap
1024
640
$00000
480
512
$03FFF

---
256-Color Palette
Reserved VRAM (512 bytes)
12-bit RGB color (2 byte entries)
Low Byte:
High Byte:
4-bit value * 17 ~ 8-bit value
e.g. $23,$01 ~ #112233
Or, truncated 8-bit ~ 4-bit value
e.g. #456789 ~ $68,$04
$1FA00
Green	Blue
0	Red
$1FBFF