How to Program in Assembly Language
for the
Lesson 16: All in the Timing

---
VSYNC Timing
- Fixed 60Hz cycle
  - 16.6666… ms
  - ~133,333 8 MHz CPU cycles
- Once per frame, at beginning.
- Requires custom IRQ handler
- Requires non-trivial math to convert to hours/minutes/seconds
  - No stored counter = No connection to real time clock

---
Instruction Timing
- Just a bunch of NOPs
  - Loops, blocks, etc.
  - 2 CPU cycles per NOP (250 ns)
- Old-school, brute-force
- Not scalable
- Only for uninterrupted, non-operational delays

---
Line Interrupts
- Granularity in-between VSYNC and NOPs
- Precise to beginning of display raster line
  - VGA:
    - 480 lines per frame
    - 31.78 μs
    - ~ 254 8 MHz CPU cycles
  - Interlaced:
    - 240 lines per frame (only even lines)
    - 63.49 μs
    - ~ 507 8 MHz CPU cycles

---
VERA Interrupt Control
- IEN (Interrupt ENable): $9F26
  - Default: $01 (VSYNC IRQ enabled)
- ISR (Interrupt Service Routine): $9F27
  - Read-only, during IRQ ISR
  - AFLOW set at startup (PCM FIFO empty)
- IRQ Line (7:0): $9F28
  - Default: $00 (IRQ Line = 0)
IRQ Line(8)	-	-	-	AFLOW	SPRCOL	LINE	VSYNC
Sprite Collisions	AFLOW	SPRCOL	LINE	VSYNC

---
Draw Vertical Line
- Assuming: 320x240 4bpp bitmap at $04000
- A: color (0-15); X: start row; Y: length; set global variable for column
column: .word 0 @set_addr: lda column lda column
start_row: .word 0 lsr column+1 clc sta $9F20 ; ADDR_L
color: .byte 0 ror column adc start_row @draw_loop:
mask: .byte 0 ldx #5 sta column lda $9F23 ; DATA0
draw_vert: @mult32: lda column+1 and mask
   sta color asl start_row adc start_row+1 ora color
   stx start_row rol start_row+1 adc #$40 sta $9F24 ; DATA1
   stz start_row+1 dex sta column+1 dey
   lda #$F0 bne @mult32 stz $9F25 ; CTRL = 0 bne @draw_loop
   sta mask lda column lda #$D0 ; stride = 160 rts
   lda #$01 clc sta $9F22 ; ADDR_H
   bit column adc start_row lda column+1
   bne @set_addr sta column sta $9F21 ; ADDR_M
   ldx #4 lda column+1 lda column
@shift_loop: adc start_row+1 sta $9F20 ; ADDR_L
   asl color sta column+1 inc $9F25 ; CTRL = 1
   lsr mask asl start_row lda #$D0 ; stride = 160
   dex rol start_row+1 sta $9F22 ; ADDR_H
   bne @shift_loop asl start_row lda column+1
        rol start_row+1 sta $9F21 ; ADDR_M

---
Example Program
Wavy Clock