How to Program in Assembly Language
for the
Lesson 9: Hello, VERA!

---
VERA: Versatile Embedded Retro Adapter
- 640x480 12-bit color graphics
  - VGA (Standard, Interlaced)
  - NTSC (Composite, S-Video)
  - 256 color palette
  - Bitmap, Tiles, Text and Sprites
- SD Card interface via SPI
- Programmable Sound Generator (PSG)
  - 16 stereo channels, 4 waveforms, variable pulse width
- Pulse Code Modulation Audio
  - Up to 48kHz 8-bit or 16-bit stereo sample playback

---
X16 Memory Map
0000	Zero Page	256 Bytes
00FF
0100	Stack	256 Bytes
01FF
0200	BASIC/Kernal RAM	1.5 kB
07FF
0800	BASIC Program	37.75 kB
9EFF
9F00	Input/Output	256 Bytes
9FFF
A000	RAM Banks	8 kB
BFFF
C000	ROM Banks	16 kB
FFFF

---
VERA Registers
- I/O Address Space: $9F20-9F3F (32 bytes)
- Only way for CPU program to control and access VERA
- Two 8-bit data channels to 17-bit VRAM address space (128 kB)
- 8-bit data channel to 4 kB PCM FIFO (write only)
- 8-bit data channel to SPI controller

---
VRAM Interface
- CTRL: $9F25
  - Set address port (ADDRSEL) in bit 0
- ADDRx_H: $9F22
  - Set bit 16 of VRAM address in bit 0
- ADDRx_M (VRAM address bits 15:8): $9F21
- ADDRx_L (VRAM address bits 7:0): $9F20
- DATA0 (read or write byte from address 0): $9F23
- DATA1 (read or write byte from address 1): $9F24
Reset (W/O)	-	-	-	-	-	DCSEL	ADDRSEL
Address Increment (Stride)	DECR	-	-	ADDR(16)

---
Reading and Writing VRAM
Copy byte from $02468 to $13579 in VRAM
VERA_addr_low = $9F20 sta VERA_addr_high
VERA_addr_high = $9F21 lda #<VRAM_SOURCE
VERA_addr_bank = $9F22 sta VERA_addr_low
VERA_data0 = $9F23 lda #1
VERA_data1 = $9F24 sta VERA_ctrl
VERA_ctrl = $9F25 lda #^VRAM_DEST
VRAM_SOURCE = $02468 sta VERA_addr_bank
VRAM_DEST = $13579 lda #>VRAM_DEST
start: sta VERA_addr_high
   stz VERA_ctrl lda #<VRAM_DEST
   lda #^VRAM_SOURCE sta VERA_addr_low
   sta VERA_addr_bank lda VERA_data0
   lda #>VRAM_SOURCE sta VERA_data1

---
VRAM Striding
- ADDRx_H: $9F22
  - Set address increment (bits 7:4) to stride for each data access
  - Set DECR (bit 3) to 1 to decrement by the stride
- Stride Values (mostly, stride = 2N-1):
Address Increment (Stride)	DECR	-	-	ADDR(16)
$0:	No Stride	$1:	1 byte	$2:	2 bytes	$3:	4 bytes
$4:	8 bytes	$5:	16 bytes	$6:	32 bytes	$7:	64 bytes
$8:	128 bytes	$9:	256 bytes	$A:	512 bytes	$B:	40 bytes
$C:	80 bytes	$D:	160 bytes	$E:	320 bytes	$F:	640 bytes

---
Writing Array to Even Addresses
Copy array bytes to even bytes in VRAM starting at $00000
VERA_addr_low = $9F20 lda #>VRAM_DEST
VERA_addr_high = $9F21 sta VERA_addr_high
VERA_addr_bank = $9F22 lda #<VRAM_DEST
VERA_data0 = $9F23 sta VERA_addr_low
VERA_ctrl = $9F25 ldx #0
VRAM_DEST = $00000 @loop:
array: .byte 8,5,12,12,15 lda array,x
start: sta VERA_data0
   stz VERA_ctrl inx
   lda #($20 | ^VRAM_DEST) cpx #(start-array)
   sta VERA_addr_bank bne @loop

---
Wait, what?

---
VERA Graphics Configuration
- DC_VIDEO: $9F29
  - Default: $21 (Layer1 Enable, Output Mode = Standard VGA)
- DC_HSCALE: $9F2A
  - Default: 128 (640 pixels wide)
- DC_VSCALE: $9F2B
  - Default: 128 (480 pixels high)
- L1_CONFIG: $9F34
  - Default: $60 (128x64 16-Color Text)
- L1_MAPBASE: $9F35
  - Default: $00 (Tile map starts at $00000 = $00 << 9)
- L1_TILEBASE: $9F36
  - Default: $7C (8x8 tiles start at $0F800 = $7C << 9)
Current Field	Sprites Enable	Layer1 Enable	Layer0 Enable	-	Chroma Disable	Output Mode
Map Height	Map Width	T256	Bitmap Mode	Color Depth
Tile Base Address (16:11)	Tile Height	Tile Width

---
Layer 1 Tilemap
1024
640
$00000
480
512
$03FFF

---
16-Color Text Map Entry
Byte 0	Character Screen Code
Byte 1	Background Color	Foreground Color
- Character Screen Code ≠ PETSCII Code ≠ ASCII Code
- Background and Foreground colors from first 16 colors in palette
ISO 8859-1
Lower/Upper
Upper/Graphics

---
Screen Code vs. PETSCII Code
00000	DF 64		08 64		08 61
00002	20 64		05 64		05 61
00004	20 64		0C 64		0C 61
00006	20 64		0C 64		0C 61
00008	20 64		0F 64		0F 61
0000A	20 64		20 64		20 64
0000C	E9 64		E9 64		E9 64
hello: .byte 72,69,76,76,79
start:
   clc
   ldx #0
   ldy #0
   jsr PLOT
@loop:
   lda hello,x
   jsr CHROUT
   inx
   cpx #5
   bne @loop
PETSCII Codes:
(with control codes)

---
8x8 1 Bit-per-Pixel (Text) Tiles
0F800	00111100
0F801	01100110
0F802	01101110
0F803	01101110
0F804	01100000
0F805	01100010
0F806	00111100
0F807	00000000
0F808	00011000
0F809	00111100
0F80A	01100110
0F80B	01111110
0F80C	01100110
0F80D	01100110
0F80E	01100110
0F80F	00000000
VRAM Addr = $0F800 + Code*8

---
256-Color Palette
Reserved VRAM (512 bytes)
12-bit RGB color (2 byte entries)
Low Byte:
High Byte:
4-bit value * 17 ~ 8-bit value
e.g. $23,$01 ~ #112233
Or, truncated 8-bit ~ 4-bit value
e.g. #456789 ~ $68,$04
$1FA00
Green	Blue
0	Red
$1FBFF

---
Example Program
1-5: Set Foreground Color
0,6-9: Set Background Color
I: Zoom In
O: Zoom Out
S: Convert @→🙂
T: Toggle Layer 1
P: Toggle Layer 0
C: Toggle Color 1 White/Black