How to Program in Assembly Language
for the
?
A
B
C
C
D
B’
ASUB
BSUB
Lesson 3: Branching and Subroutines
Lesson 3: Branching and Subroutines

---
Flow Control: C vs. Assembly
- C: if, while, for, switch, etc.
- Assembly: BEQ, BMI, BVS, BCS, etc.
Assembly:
C:
if (val == 5) {
  val++;
} else {
  val--;
}
return;
   lda val
   cmp #5
   beq incval
   dec val
   bra done
incval:
   inc val
done:
   rts

---
Relative Addressing
- Required by all branching instructions
- Target must be between PC-128 and PC+127
Invalid:
Fixed:
Valid:
.org $1000
behind:
   nop
.org $107F
   beq behind
   bra ahead
.org $1103
ahead:
   nop
.org $1000
behind:
   nop
.org $107F
   beq gobehind
   jmp ahead
gobehind:
   jmp behind
.org $1103
ahead:
   nop
.org $1000
behind:
   nop
.org $107E
   beq behind
   bra ahead
.org $1101
ahead:
   nop

---
Status Register (P)
- Status bits changed by certain instructions
- Bitmap: NV-BDIZC
Bit	Label	Meaning if set	Branch if set	Branch if clear
7	N	Result negative (bit 7 set)	BMI	BPL
6	V	Overflow occurred during arithmetic instruction	BVS	BVC
5	N/A	Unused	N/A	N/A
4	B	BRK instruction triggered interrupt	N/A	N/A
3	D	Binary-coded Decimal (BCD) mode enabled	N/A	N/A
2	I	Interrupts disabled	N/A	N/A
1	Z	Result zero	BEQ	BNE
0	C	Arithmetic instruction resulted in carry	BCS	BCC

---
Compare Instructions
- Compares memory value with accumulator (CMP) or index register (CPX, CPY)
- Performs subtraction of register value with memory value, without storing numerical result, only affecting N, Z and C status bits
Instruction	N	Z	C
lda #5	0	0	?
cmp #4	0	0	1
cmp #5	0	1	1
cmp #6	1	0	0

---
Changing Status Flags
- Status flags used for branching (N,V,Z,C) can be... set directly (CLC, SEC, CLV)
- ...pulled from stack (PLP)
- ...through load and math instructions
Instruction	A	(S)	N	V	Z	C
lda #$C1	C1	??	1	?	0	?
pha	C1	C1	1	?	0	?
plp	C1	??	1	1	0	1
clc	C1	??	1	1	0	0
clv	C1	??	1	0	0	0
lda #0	00	??	0	0	1	0
adc #127	7F	??	0	0	0	0
adc #1	80	??	1	1	0	0
adc #127	FF	??	1	0	0	0
adc #1	00	??	0	0	1	1

---
Indexed Loop: C vs. Assembly
- C: for loop
- Assembly: branching on index comparison
Assembly:
C:
for(i=0; i<4; i++) {
  foo[i] = bar[i];
}
   ldx #0
loop:
   lda bar,x
   sta foo,x
   inx
   cpx #4
   bmi loop

---
Functions: C vs. Assembly
- C: functions with arguments and return values on stack
- Assembly: subroutines with return addresses only on stack
Assembly:
C:
void incval() {
  val++;
}
…
  incval();
incval:
   inc val
   rts
…
   jsr incval

---
Commander X16 Kernal
Based on Commodore Kernal for PET, VIC-20, C-64
Re-uses most of jump table and all original addresses
Subroutines in ROM
Uses registers and zero page for arguments, return values
Assembly:
C:
CHROUT = $FFD2
   lda #$35
   jsr CHROUT
#include <stdio.h>
putc(0x35, stdout);

---
Example Program
CHROUT = $FFD2
NEWLINE = $0D
   jmp start
data:
.byte $01,$23,$45,$67,$89,$AB,$CD,$EF

---
Example Program, continued
start:
   ; branching if less than (N set)
   ldx #0
n_loop:
   lda data,x
   cmp #$55
   bmi next_n
   txa
   ora #$30
   jsr CHROUT
next_n:
   inx
   cpx #8
   bne n_loop
   lda #NEWLINE
   jsr CHROUT

---
Example Program, continued
   ; branching if carry (C set)
   ldx #0
c_loop:
   lda data,x
   clc
   adc #$55
   bcs next_c
   txa
   ora #$30
   jsr CHROUT
next_c:
   inx
   cpx #8
   bne c_loop
   lda #NEWLINE
   jsr CHROUT

---
Example Program, continued
   ; branching if overflow (V set)
   ldx #0
v_loop:
   lda data,x
   clc
   adc #$55
   bvs next_v
   txa
   ora #$30
   jsr CHROUT
next_v:
   inx
   cpx #8
   bne v_loop
   lda #NEWLINE
   jsr CHROUT
   rts