How to Program in Assembly Language
for the
Lesson 5: The Stack

---
X16 Memory Map
0000	Zero Page	256 Bytes
00FF
0100	Stack	256 Bytes
01FF
0200	BASIC/Kernal RAM	1.5 kB
07FF
0800	BASIC Program	37.75 kB
9EFF
9F00	Input/Output	256 Bytes
9FFF
A000	RAM Banks	8 kB
BFFF
C000	ROM Banks	16 kB
FFFF

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	??
1FE	??
1FF	??
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
????	??	??	1000	??	??

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	??
1FE	??
1FF	??
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
1000	??	??	1002	??	FF

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	??
1FE	??
1FF	??
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
1002	??	FF	1003	FF	FF

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	??
1FE	??
1FF	FF
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
1003	FF	FF	1004	FE	FF

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	06
1FE	10
1FF	FF
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
1004	FE	FF	1009	FC	FF

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	06
1FE	10
1FF	FF
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
1009	FC	FF	100A	FC	FC

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	06
1FE	10
1FF	FF
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
100A	FC	FC	1007	FE	FC

---
Stack Behavior
Push: Store to stack top, decrement Stack Pointer
Pull: Load from below stack top, increment Stack Pointer
.org $1000
   ldx #$FF
   txs
   phx
   jsr foo
   plx
   brk
foo:
   tsx
   rts
STACK
1FC	??
1FD	06
1FE	10
1FF	FF
1000
1002
1003
1004
1007
1008
1009
100A
IN			OUT
PC	SP	X	PC	SP	X
1007	FE	FC	1008	FF	FF

---
JSR: Jump to SubRoutine
- Mode: Absolute
- PCOUT = Address
- SPOUT = SPIN - 2
- *(SPIN) = (PCIN + 2) >> 8
- *(SPIN - 1) = (PCIN + 2) & 255

---
RTS: ReTurn from Subroutine
- Mode: Implied
- PCOUT = *(SPIN + 1) | (*(SPIN + 2) << 8) + 1
- SPOUT = SPIN + 2

---
RTI: ReTurn from Interrupt
- Mode: Implied
- SROUT = *(SPIN + 1)
- PCOUT = *(SPIN + 2) | (*(SPIN + 3) << 8)
- SPOUT = SPIN + 3

---
Push Instructions
- All store byte from register value to stack top then decrement SP
- All support only Implied mode
- PHA: PusH Accumulator
- PHX*: PusH X index register
- PHY*: PusH Y index register
- PHP: PusH Processor status register
* Added for 65C02

---
Pull Instructions
- All load byte into register from immediately below stack top then increment SP
- All make no change to stack RAM
- All support only Implied mode
- PLA: PuLl Accumulator
- PLX*: PuLl X index register
- PLY*: PuLl Y index register
- PLP: PuLl Processor status register
* Added for 65C02

---
Transfer Instructions
- All do not affect stack RAM
- All support only Implied mode
- TSX: Transfer Stack pointer to X index register
  - Loads low byte of SP into X
  - Does not change SP
- TXS: Transfer X index register to Stack pointer
  - Loads value of X into SP low byte
  - DANGER: Can set SP to any address on stack page!
    - Don’t use on X16 unless you are OK breaking BASIC!

---
Be Careful!
- Data MUST be pulled from the stack in the reverse order it was pushed
- Anything pushed to the stack during a subroutine or interrupt service routine (ISR) MUST be pulled out before returning, but don’t overpull!
- You only have 256 bytes. Recursion is not the best way to avoid stack overflows!
- Leave room at the top (at least 6 bytes) for ISRs at any time

---
Example Program
CHROUT = $FFD2
NEWLINE = $0D
SPACE = $20
   jmp start
header: .asciiz " a x y sp sr"
start:
   ldx #0
@header_loop:
   lda header,x
   beq @header_done
   jsr CHROUT
   inx
   bra @header_loop
@header_done:
   lda #NEWLINE
   jsr CHROUT

---
Example Program, continued
   jsr print_regs
   lda #$12
   ldx #$34
   ldy #$56
   jsr print_regs
   pha
   jsr print_regs
   tsx
   jsr print_regs
   php
   jsr print_regs
   ply
   jsr print_regs
   plp
   jsr print_regs
   rts

---
Example Program, continued
print_regs:
   pha
   phx
   php
   jsr print_hex
   lda #SPACE
   jsr CHROUT
   txa
   jsr print_hex
   lda #SPACE
   jsr CHROUT
   tya
   jsr print_hex
   lda #SPACE
   jsr CHROUT

---
Example Program, continued
   tsx
   txa
   clc
   adc #5 ; calculate SP from before JSR
   jsr print_hex
   lda #SPACE
   jsr CHROUT
   pla ; pull earlier P into A
   pha ; push it again to pull back into P later
   jsr print_hex
   lda #SPACE
   jsr CHROUT
   lda #NEWLINE
   jsr CHROUT
   plp
   plx
   pla
   rts