How to Program in Assembly Language
for the
How to Program in Assembly Language
Lesson 18: Sprites
Lesson 18: Sprites
Lesson 18: Sprites

---
VERA Sprites
} Z3
Sprite i
- 128 Independent Sprites
- Variable Dimensions (8, 16, 32, 64 pixels)
- 16 colors (4bpp) or 256 colors (8bpp)
- Place anywhere on 640x480 display
- Assets stored at arbitrary VRAM locations
- 3 Z-levels, index-based priority
- Line limit: based on sprite widths, color depths
- Collision-driven interrupts
Sprite i+n
Layer 1
} Z2
Sprite j
Sprite j+n
Layer 0
} Z1
Sprite k
Sprite k+n
Background

---
VERA Registers
- IEN (Interrupt ENable): $9F26
  - Bit 2 set: enable sprite collision IRQ
- ISR (Interrupt Service Routine): $9F27
  - Bit 2 set on first IRQ after collision (latches)
  - Bits 7:4 - Current collisions (whenever occurring)
- DC_VIDEO: $9F29
  - Bit 6 set: enable all sprites in Z1, Z2, Z3
IRQ Line(8)	-	-	-	AFLOW	SPRCOL	LINE	VSYNC
Sprite Collisions	AFLOW	SPRCOL	LINE	VSYNC
Current Field	Sprites Enable	Layer1 Enable	Layer0 Enable	-	Chroma Disable	Output Mode

---
VRAM Sprite Attributes
- VRAM $1FC00-1FFFF
  - 8 bytes per sprite; starting address = $1FC00 + 8 * sprite index
- Bytes 0-1: Asset Address, Mode
  - Mode: 0 = 4bpp (16-color); 1 = 8bpp (256-color)
- Bytes 2-5: X,Y Coordinates (10 bits, little-endian)
  - X: -63 to 639; Y: -63 to 479
- Byte 6: Collision, Z-level, Flipping
  - Collision Mask: Set bit for each collision “class”
  - Z-level: 0 = off; 1 = behind layers; 2 = between layers; 3 = in front of layers
  - V/H-Flip: Set = Flipping enabled
- Byte 7: Dimensions, Palette Offset
  - Sprite Height/Width: 0 = 8 pixels; 1 = 16 pixels; 2 = 32 pixels; 3 = 64 pixels
  - Palette Offset: 0-15; Sprite color index 0 = Palette color index (16 * offset)
Address (12:5)
Mode	-	-	-	Address (16:13)
Collision Mask	Z-Level	V-Flip	H-Flip
Sprite Height	Sprite Width	Palette Offset

---
Mode 0 Sprites
4bpp (16 colors), 4-bit palette offset
Change offset for different looks
0
16
32
48
Offset 0:
Offset 1:
Offset 2:
Offset 3:

---
Mode 1 Sprites
{
8bpp, full 256-color palette
Twice the VRAM, VERA work units
64x64
{
64x64
Custom Palette

---
Placing a Sprite
Define sprite in RAM, copy to VRAM, place as sprite 1 on screen @ 150,100
VERA_CTRL = $9F25 place_ball: lda #($10 | ^SPRITE1_ATTR)
VERA_BANK = $9F22 stz VERA_CTRL sta VERA_BANK
VERA_HIGH = $9F21 lda #($10 | ^VRAM_BALL) lda #>SPRITE1_ATTR
VERA_LOW = $9F20 sta VERA_BANK sta VERA_HIGH
VERA_DATA0 = $9F23 lda #>VRAM_BALL lda #<SPRITE1_ATTR
VRAM_BALL = $04560 sta VERA_HIGH sta VERA_LOW
SPRITE1_ATTR = $1FC08 lda #<VRAM_BALL lda #<(VRAM_BALL >> 5)
ag_ball: sta VERA_LOW sta VERA_DATA0
.byte $00,$69,$95,$00 ldx #0 lda #>(VRAM_BALL >> 5)
.byte $05,$8b,$dc,$80 @asset_loop: sta VERA_DATA0
.byte $26,$9e,$ff,$d2 lda ag_ball,x lda #150
.byte $35,$ad,$ff,$c6 sta VERA_DATA0 sta VERA_DATA0
.byte $24,$9c,$ef,$a5 inx stz VERA_DATA0
.byte $13,$69,$bb,$81 cpx #32 lda #100
.byte $01,$35,$77,$40 bne @asset_loop sta VERA_DATA0
.byte $00,$12,$21,$00 stz VERA_DATA0
        lda #$0C
        sta VERA_DATA0
        lda #$01
        sta VERA_DATA0
        rts

---
Sprite Collision
- When two sprites intersect while IEN[SPRCOL] is set:
  - ISR[Collision Mask] = Sprite1[Collision Mask] & Sprite1[Collision Mask]
  - ISR[SPRCOL] = 1
  - Trigger IRQ
 Mario[CM] = %0011
  Coin[CM] = %1010
Goomba[CM] = %0101
ISR[CM] = %0001
ISR[CM] = %0010

---
Mouse Cursor
- Sprite 0 used for mouse cursor when enabled
- MOUSE_CONFIG with A = 0: Mouse Disabled
  - Sprite 0 available for other use (with caution!)
- MOUSE_CONFIG with A = 1: Default Cursor
  - No need to configure attributes
- MOUSE_CONFIG with A = $FF: Custom Cursor
  - Cursor asset needed in VRAM, attributes set to use it

---
Example Program:
Amiga X16 Balls
Mouse with animated cursor
Shadow sprite in reflected position
Beep on collision