How to Program in Assembly Language
for the
Lesson 6: A Bit Advanced

---
Branching on Bits
- Do different processing based on particular bit states
- Example: Determine whether input character code is even or odd
Setup:
Bit Logic:
Holistic Logic:
CHRIN = $FFCF
CHROUT = $FFD2
yes: .byte “y”
no: .byte “n”
iseven:
   jsr CHRIN
bit #$01
; A unchanged
and #$01
; A = 0 or 1
Big Finish:
   beq @even
   lda no
   bra @print
@even:
   lda yes
@print:
   jsr CHROUT
   rts

---
BIT: test BITs in memory
- Modes:
  - Immediate:	bit #$12
    - Only affects Z for 65C02
  - Absolute:	bit $1234
  - Absolute Indexed with X*: bit $1234,x
  - Zero Page:	bit $34
  - Zero Page Indexed with X*: bit $34,x
- N = MemVal & 128 == 128 (i.e. Bit 7 set)
- V = MemVal & 64 == 64 (i.e. Bit 6 set)
- Z = A & MemVal == 0
- A,C: Unaffected
* Added for 65C02

---
Branching on Bits 2: Make It So
- Do different processing based on particular bit states
- Example: Determine whether input character code is even or odd
Setup:
Modify:
Store Original:
trb input
; input = input & $FE
CHRIN = $FFCF
CHROUT = $FFD2
yes: .byte “y”
no: .byte “n”
input: .byte 0
iseven:
   jsr CHRIN
   sta input
   lda #$01
bit input
; input unchanged
Big Finish:
   beq @even
   lda no
   bra @print
@even:
   lda yes
@print:
   jsr CHROUT
   rts

---
TRB: Test and Reset Bits
- Added for 65C02
- Modes:
  - Absolute:	trb $1234
  - Zero Page:	trb $34
- Z = A & MemVal == 0
- MemVal = MemVal & (A ^ 255)
  - Bits set in A will be cleared at memory location
- A,N,V,C: Unaffected

---
TSB: Test and Set Bits
- Added for 65C02
- Modes:
  - Absolute:	tsb $1234
  - Zero Page:	tsb $34
- Z = A & MemVal == 0
- MemVal = MemVal | A
  - Bits set in A will be set at memory location
- A,N,V,C: Unaffected

---
Branching on Bits 3: Singularity
- Do different processing based on particular bit states
- Example: Determine whether input character code is even or odd
Setup:
65C02:
6502:
bbr0 INPUT, @even
lda #$01
bit INPUT
beq @even
CHRIN = $FFCF
CHROUT = $FFD2
INPUT = $30
yes: .byte “y”
no: .byte “n”
iseven:
   jsr CHRIN
   sta INPUT
Big Finish:
   lda no
   bne @print
@even:
   lda yes
@print:
   jsr CHROUT
   rts
3 bytes
5 cycles
6 bytes
7-9 cycles

---
BBRn: Branch on Bit Reset n
- Added for 65C02
- Different opcodes for bits 0-7
- Mode: Zero Page and Relative… AT THE SAME TIME!
  - Example: bbr4 $30,label
- Branch to relative address if bit n is clear
- Always 5 cycles, no penalty for branching or page crossing
- Memory,A,N,V,Z,C: Unaffected

---
BBSn: Branch on Bit Set n
- Added for 65C02
- Different opcodes for bits 0-7
- Mode: Zero Page and Relative… AT THE SAME TIME!
  - Example: bbs4 $30,label
- Branch to relative address if bit n is set
- Always 5 cycles, no penalty for branching or page crossing
- Memory,A,N,V,Z,C: Unaffected

---
Branching on Bits 4: Make It So, But Faster!
- Do different processing based on particular bit states
- Example: Determine whether input character code is even or odd
Setup:
65C02:
6502:
rmb0 INPUT
pha
and #$FE
sta INPUT
pla
CHRIN = $FFCF
CHROUT = $FFD2
INPUT = $30
yes: .byte “y”
no: .byte “n”
iseven:
   jsr CHRIN
   sta INPUT
Big Finish:
   bit #$01
   beq @even
   lda no
   bne @print
@even:
   lda yes
@print:
   jsr CHROUT
   rts
2 bytes
5 cycles
6 bytes
13 cycles

---
RMBn: Reset Memory Bit n
- Added for 65C02
- Different opcodes for bits 0-7
- Mode: Zero Page
  - Example: rmb4 $30
- MemVal = MemVal & ((1 << n) ^ 255)
  - Bit n cleared at Zero Page address
- A,N,V,Z,C: Unaffected

---
SMBn: Set Memory Bit n
- Added for 65C02
- Different opcodes for bits 0-7
- Mode: Zero Page
  - Example: smb4 $30
- MemVal = MemVal | (1 << n)
  - Bit n set at Zero Page address
- A,N,V,Z,C: Unaffected

---
Example Program
; Zero Page
CODE = $30
; Kernal
CHRIN = $FFCF
CHROUT = $FFD2
; PETSCII
NEWLINE = $0D
WHITE = $05
SPACE = $20
LT_RED = $96
LT_GREEN = $99
LT_GRAY = $9B
; Constants
MAX_INPUT = 40
   jmp start
input: .res MAX_INPUT
size: .byte 0

---
Example Program, continued
start:
   ldx #0
@read:
   jsr CHRIN
   cmp #NEWLINE
   beq @done
   sta input,x
   inx
   cpx #MAX_INPUT
   bne @read
@done:
   stx size
   lda #NEWLINE
   jsr CHROUT

---
Example Program, continued
   ldx #0
print:
   lda input,x
   sta CODE
   bit CODE
   bmi @gray
   bbs6 CODE,@green
   lda #LT_RED
   bra @print_code
@green:
   lda #LT_GREEN
   bra @print_code

---
Example Program, continued
@gray:
   lda #LT_GRAY
@print_code:
   jsr CHROUT
   lda CODE
   jsr CHROUT
   inx
   cpx size
   bmi print
   lda #NEWLINE
   jsr CHROUT

---
Example Program, continued
   lda #WHITE
   jsr CHROUT
   lda input
   sta CODE
   jsr print_hex
   lda #SPACE
   jsr CHROUT
   lda CODE
   jsr CHROUT
   lda #NEWLINE
   jsr CHROUT

---
Example Program, continued
   lda #$80
   tsb CODE
   beq @red
   lda #LT_GRAY
   bra @print_mod
@red:
   lda #LT_RED
@print_mod:
   jsr CHROUT
   lda CODE
   jsr print_hex
   lda #SPACE
   jsr CHROUT
   lda CODE
   jsr CHROUT

---
Example Program, continued
   lda #NEWLINE
   jsr CHROUT
   lda #LT_GREEN
   jsr CHROUT
   rmb7 CODE
   lda CODE
   jsr print_hex
   lda #SPACE
   jsr CHROUT
   lda CODE
   jsr CHROUT
   lda #WHITE
   jsr CHROUT
   rts