How to Program in Assembly Language
for the
Lesson 7: The Rest

---
LDA: LoaD Accumulator
  - Zero Page:	lda $34
  - Zero Page,X:	lda $34,x
  - Zero Page Indirect*:	lda ($34)
  - Zero Page,X Indirect:	lda ($34,x)
  - Zero Page Indirect,Y: lda ($34),y
- Modes:
  - Immediate:	lda #$12
  - Absolute:	lda $1234
  - Absolute,X:	lda $1234,x
  - Absolute,Y:	lda $1234,y
- A = MemVal
- N = MemVal & 128 == 128 (i.e. Bit 7 set)
- Z = MemVal == 0
* Added for 65C02

---
STA: STore Accumulator
  - Zero Page,X:	sta $34,x
  - Zero Page Indirect*:	sta ($34)
  - Zero Page,X Indirect:	sta ($34,x)
  - Zero Page Indirect,Y: sta ($34),y
- Modes:
  - Absolute:	sta $1234
  - Absolute,X:	sta $1234,x
  - Absolute,Y:	sta $1234,y
  - Zero Page: sta $34
- MemVal = A
- No status bits affected

---
LDX, LDY: LoaD X, Y
- Modes (available for both LDX and LDY):
  - Immediate:	ldx #$12 ldy #$12
  - Absolute:	ldx $1234 ldy $1234
  - Zero Page:	ldx $34 ldy $34
- Modes for LDX only:
  - Absolute,Y:	ldx $1234,y
  - Zero Page,Y:	ldx $34,y
- X = MemVal, Y = MemVal
- N = MemVal & 128 == 128 (i.e. Bit 7 set)
- Z = MemVal == 0
- Modes for LDY only:
  - Absolute,X:	ldy $1234,x
  - Zero Page,X:	ldy $34,x

---
STX, STY: STore X, Y
- Modes (available for both STX and STY):
  - Absolute:	stx $1234 sty $1234
  - Zero Page:	stx $34 sty $34
- Modes for STX only:
  - Absolute,Y:	stx $1234,y
  - Zero Page,Y:	stx $34,y
- MemVal = X, MemVal = Y
- No status bits affected
- Modes for STY only:
  - Absolute,X:	sty $1234,x
  - Zero Page,X:	sty $34,x

---
Example Program
; Zero Page
CODE = $30
; Kernal
CHRIN = $FFCF
CHROUT = $FFD2
; PETSCII
NEWLINE = $0D
SPACE = $20
; Constants
MAX_INPUT = 40
   jmp start
input: .res MAX_INPUT
size: .byte 0

---
Example Program, continued
   rts