How to Program in Assembly Language
for the
Lesson 15: Bitmap

---
VERA Bitmap Modes
- Each VERA layer can be any tile or bitmap mode
- 320 or 640 pixels wide
- Variable color depth, one palette offset per layer
  - 1bpp, 2-color graphics
  - 2bpp, 4-color graphics
  - 4bpp, 16-color graphics
  - 8bpp, 256-color graphics
- No scrolling

---
Bitmap Widths
- 320-pixel bitmaps repeated horizontally when screen width > 320
- 640-pixel bitmaps cropped to corner when screen width < 640
640 x 480
320 x 240
320 x 240
640 x 480

---
Bitmap Layer Configuration
- L0_CONFIG: $9F2D; L1_CONFIG: $9F34
  - Map Height/Width: Unused
  - T256: Unused
  - Bitmap Mode: 1 = bitmap mode
  - Color Depth: 0 = 1bpp; 1 = 2bpp; 2 = 4bpp; 3 = 8bpp
- L0_TILEBASE: $9F2F; L1_TILEBASE: $9F36
  - Tile Base Address: Bitmap address >> 11 (2kB alignment)
  - Tile Height: Unused
  - Tile Width: 0 = 320 pixels; 1 = 640 pixels
- L0_HSCROLL_H: $9F31; L1_HSCROLL_H: $9F38
  - H-Scroll (11:8): Palette offset (0-15)
Map Height	Map Width	T256	Bitmap Mode	Color Depth
Tile Base Address (16:11)	Tile Height	Tile Width
Unused	H-Scroll (11:8)

---
1bpp Bitmap
- Each byte: 8 pixels
  - 320x240 bitmap: 9600 bytes
  - 640x480 bitmap: 37.5 kB
- Colors: First two of any 16-color palette offset
  - Default:
  - 0: Always Transparent
  - 1: Remapped to 17, 33, 49, etc.
- Good enough for…
  - Original Macintosh!
  - GEOS!
0	1	0	1	1	0	1	0
5A

---
Higher Color Depths
2bpp / 4 colors / Each byte: 4 pixels / 320x240: 18.75 kB / 640x480: 75 kB	4bpp / 16 colors / Each byte: 2 pixels / 320x240: 37.5 kB / 640x480: 150 kB / 640x404: 126.25 kB	8bpp / 256 colors (full palette) / Each byte: 1 pixel / 320x240: 75 kB / 640x480: 300 kB / 640x202: 126.25 kB

---
Palette Offsets
- All bitmaps require specific palette offset (0-15)
- Color index 0 transparent regardless of depth or offset
- 8bpp: Color indexes 1-15 remapped if non-zero offset, 16-255 unchanged
Transparent
PO 0
PO 1
PO 2
PO 3
PO 4
PO 5
PO 6
PO 7
PO 8
PO 9
PO 10
PO 11
PO 12
PO 13
PO 14
PO 15
0	0	0	2	2	0	0	0
0	0	2	8	8	2	0	0
0	2	8	7	7	8	2	0
2	8	7	5	5	7	8	2
8	7	5	6	6	5	7	8
7	5	6	4	4	6	5	7
5	6	4	0	0	4	6	5
6	4	0	0	0	0	4	6
0	0	0	2	2	0	0	0
0	0	2	8	8	2	0	0
0	2	8	7	7	8	2	0
2	8	7	5	5	7	8	2
8	7	5	6	6	5	7	8
7	5	6	4	4	6	5	7
5	6	4	0	0	4	6	5
6	4	0	0	0	0	4	6
0	0	0	2	2	0	0	0
0	0	2	8	8	2	0	0
0	2	8	7	7	8	2	0
2	8	7	5	5	7	8	2
8	7	5	6	6	5	7	8
7	5	6	4	4	6	5	7
5	6	4	0	0	4	6	5
6	4	0	0	0	0	4	6
PO 0 PO 1 PO 15
1bpp
2bpp
4bpp

---
Draw Vertical Line
- Assuming: 320x240 4bpp bitmap at $04000
- A: color (0-15); X: start row; Y: length; set global variable for column
column: .word 0 @set_addr: lda column lda column
start_row: .word 0 lsr column+1 clc sta $9F20 ; ADDR_L
color: .byte 0 ror column adc start_row @draw_loop:
mask: .byte 0 ldx #5 sta column lda $9F23 ; DATA0
draw_vert: @mult32: lda column+1 and mask
   sta color asl start_row adc start_row+1 ora color
   stx start_row rol start_row+1 adc #$40 sta $9F24 ; DATA1
   stz start_row+1 dex sta column+1 dey
   lda #$F0 bne @mult32 stz $9F25 ; CTRL = 0 bne @draw_loop
   sta mask lda column lda #$D0 ; stride = 160 rts
   lda #$01 clc sta $9F22 ; ADDR_H
   bit column adc start_row lda column+1
   bne @set_addr sta column sta $9F21 ; ADDR_M
   ldx #4 lda column+1 lda column
@shift_loop: adc start_row+1 sta $9F20 ; ADDR_L
   asl color sta column+1 inc $9F25 ; CTRL = 1
   lsr mask asl start_row lda #$D0 ; stride = 160
   dex rol start_row+1 sta $9F22 ; ADDR_H
   bne @shift_loop asl start_row lda column+1
        rol start_row+1 sta $9F21 ; ADDR_M

---
Example Program
Fading Cycle