How to Program in Assembly Language
for the
Lesson 9: Hello, VERA!

---
VERA: Versatile Embedded Retro Adapter
- 640x480 12-bit color graphics
  - VGA (Standard, Interlaced)
  - NTSC (Composite, S-Video)
  - 256 color palette
  - Bitmap, Tiles, Text and Sprites
- SD Card interface via SPI
- Programmable Sound Generator (PSG)
  - 16 stereo channels, 4 waveforms, variable pulse width
- Pulse Code Modulation Audio
  - Up to 48kHz 8-bit or 16-bit stereo sample playback

---
X16 Memory Map
0000	Zero Page	256 Bytes
00FF
0100	Stack	256 Bytes
01FF
0200	BASIC/Kernal RAM	1.5 kB
07FF
0800	BASIC Program	37.75 kB
9EFF
9F00	Input/Output	256 Bytes
9FFF
A000	RAM Banks	8 kB
BFFF
C000	ROM Banks	16 kB
FFFF

---
VERA Registers
- I/O Address Space: $9F20-9F3F (32 bytes)
- Only way for CPU program to control and access VERA
- Two 8-bit data channels to 17-bit VRAM address space (128 kB)
- 8-bit data channel to 4 kB PCM FIFO (write only)
- 8-bit data channel to SPI controller

---
VRAM Interface
- CTRL: $9F25
  - Set address port (ADDRSEL) in bit 0
- ADDRx_H: $9F22
  - Set bit 16 of VRAM address in bit 0
- ADDRx_M (VRAM address bits 15:8): $9F21
- ADDRx_L (VRAM address bits 7:0): $9F20
- DATA0 (read or write byte from address 0): $9F23
- DATA1 (read or write byte from address 1): $9F24
Reset (W/O)	-	-	-	-	-	DCSEL	ADDRSEL
Address Increment (Stride)	DECR	-	-	ADDR(16)

---
Reading and Writing VRAM
Copy byte from $02468 to $13579 in VRAM
VERA_addr_low = $9F20 sta VERA_addr_high
VERA_addr_high = $9F21 lda #<VRAM_SOURCE
VERA_addr_bank = $9F22 sta VERA_addr_low
VERA_data0 = $9F23 lda #1
VERA_data1 = $9F24 sta VERA_ctrl
VERA_ctrl = $9F25 lda #^VRAM_DEST
VRAM_SOURCE = $02468 sta VERA_addr_bank
VRAM_DEST = $13579 lda #>VRAM_DEST
start: sta VERA_addr_high
   stz VERA_ctrl lda #<VRAM_DEST
   lda #^VRAM_SOURCE sta VERA_addr_low
   sta VERA_addr_bank lda VERA_data0
   lda #>VRAM_SOURCE sta VERA_data1

---
VRAM Striding
- ADDRx_H: $9F22
  - Set address increment (bits 7:4) to stride for each data access
  - Set DECR (bit 3) to 1 to decrement by the stride
- Stride Values (mostly, stride = 2N-1):
Address Increment (Stride)	DECR	-	-	ADDR(16)
$0:	No Stride	$1:	1 byte	$2:	2 bytes	$3:	4 bytes
$4:	8 bytes	$5:	16 bytes	$6:	32 bytes	$7:	64 bytes
$8:	128 bytes	$9:	256 bytes	$A:	512 bytes	$B:	40 bytes
$C:	80 bytes	$D:	160 bytes	$E:	320 bytes	$F:	640 bytes

---
Writing Array to Even Addresses
Copy array bytes to even bytes in VRAM starting at $00000
VERA_addr_low = $9F20 lda #>VRAM_DEST
VERA_addr_high = $9F21 sta VERA_addr_high
VERA_addr_bank = $9F22 lda #<VRAM_DEST
VERA_data0 = $9F23 sta VERA_addr_low
VERA_ctrl = $9F25 ldx #0
VRAM_DEST = $00000 @loop:
array: .byte 8,5,12,12,15 lda array,x
start: sta VERA_data0
   stz VERA_ctrl inx
   lda #($20 | ^VRAM_DEST) cpx #(start-array)
   sta VERA_addr_bank bne @loop

---
Wait, what?

---
VERA Graphics Configuration
- DC_VIDEO: $9F29
  - Default: $21 (Layer1 Enable, Output Mode = Standard VGA)
- DC_HSCALE: $9F2A
  - Default: 128 (640 pixels wide)
- DC_VSCALE: $9F2B
  - Default: 128 (480 pixels high)
- L1_CONFIG: $9F34
  - Default: $60 (128x64 16-Color Text)
- L1_MAPBASE: $9F35
  - Default: $00 (Tile map starts at $00000 = $00 << 9)
- L1_TILEBASE: $9F36
  - Default: $7C (8x8 tiles start at $0F800 = $7C << 9)
Current Field	Sprites Enable	Layer1 Enable	Layer0 Enable	-	Chroma Disable	Output Mode
Map Height	Map Width	T256	Bitmap Mode	Color Depth
Tile Base Address (16:11)	Tile Height	Tile Width

---
Layer 1 Tilemap
1024
640
$00000
480
512
$03FFF

---
16-Color Text Map Entry
Byte 0	Character Screen Code
Byte 1	Background Color	Foreground Color
- Character Screen Code ≠ PETSCII Code ≠ ASCII Code
- Background and Foreground colors from first 16 colors in palette
ISO 8859-1
Lower/Upper
Upper/Graphics

---
Example Program