How to Program in Assembly Language
for the
Lesson 17: FM Synthesis

---
Yamaha YM2151
- Also known as the FM Operator Type-M (OPM)
- 8 stereo voices
- 4-function Frequency Modulation
- Noise generator
- 8 octave range

---
Register Interface
- Wait for Write Ready
  - Read $9FE1
  - Bit 7 clear
- Set register address
  - Write $9FE0
- Set register value
  - Write $9FE1

---
Defining Instruments
- Write “Patch” configuration parameters for channel on each function.
  - Functions: M1, C1, M2, C2
- Set channel control registers
  - Right/Left Channels, Feedback Level
  - Function Connections:

---
Playing Notes
- Key On (KON) Register: $08
  - Bits 6:3 – Functions Enabled (C2, M2, C1, M1)
    - All clear = Key Off
  - Bits 2:0 – Channel Number (0-7)
- Key Code (KC) Register: $28-$2F (per channel)
  - Bits 6:4 – Octave (0-7)
  - Bits 3:0 – Chromatic Note (0-2,4-6,8-10,12-14 → C# to C)
  - $3E = Middle C
- Key Fraction (KF) Register: $30-$37 (per channel)
  - Bits 7:2 – Fraction (0-63 → 0 to 98.4 cents higher)

---
Repeating a Note
Play Middle C on second channel for half second, rest half second, repeat 10 times
YM_REG = $9FE0 lda #KON ldy #30
YM_DATA = $9FE1 sta YM_REG @wait_on_loop:
KON = $08 lda #CH2 wai
ALL_ON = $78 sta YM_DATA dey
CH2 = $01 lda #(KC | CH2) bne @wait_on_loop
KC = $28 sta YM_REG lda #$3E sta VERA_data0
MIDDLE_C = $3E lda #MIDDLE_C sta VERA_data0 lda #$80
        sta YM_DATA lda #$05 sta VERA_data0
ostinato: lda #KON
   ldx #10 sta YM_REG
@cycle_loop: lda #(ALL_ON | CH2) sta VERA_data0 lda #$29
   bit YM_DATA sta YM_DATA lda #$40 sta VERA_data0
   bmi @cycle_loop sta VERA_data0 lda #($40 | 16)

---
Example Program:
Waveform Demo
Sweep pulse frequency from Middle C up and back down
Sweep pulse width from 50% to minimum and back
Change to sawtooth, sweep up and down
Change to triangle, sweep up and down
Change to noise, sweep up and down
Extra Program: Piano