How to Program in Assembly Language
for the
How to Program in Assembly Language
Lesson 18: Sprites
Lesson 18: Sprites
Lesson 18: Sprites

---
VERA Sprites
} Z3
Sprite i
- 128 Independent Sprites
- Variable Dimensions (8, 16, 32, 64 pixels)
- 16 colors (4bpp) or 256 colors (8bpp)
- Place anywhere on 640x480 display
- Assets stored at arbitrary VRAM locations
- 3 Z-levels, index-based priority
- Line limit: based on sprite widths, color depths
- Collision-driven interrupts
Sprite i+n
Layer 1
} Z2
Sprite j
Sprite j+n
Layer 0
} Z1
Sprite k
Sprite k+n
Background

---
VERA Registers
- IEN (Interrupt ENable): $9F26
  - Bit 2 set: enable sprite collision IRQ
- ISR (Interrupt Service Routine): $9F27
  - Bit 2 set on first IRQ after collision (latches)
  - Bits 7:4 - Current collisions (whenever occurring)
- DC_VIDEO: $9F29
  - Bit 6 set: enable all sprites in Z1, Z2, Z3
IRQ Line(8)	-	-	-	AFLOW	SPRCOL	LINE	VSYNC
Sprite Collisions	AFLOW	SPRCOL	LINE	VSYNC
Current Field	Sprites Enable	Layer1 Enable	Layer0 Enable	-	Chroma Disable	Output Mode

---
VRAM Sprite Attributes
- VRAM $1FC00-1FFFF
  - 8 bytes per sprite; starting address = $1FC00 + 8 * sprite index
- Bytes 0-1: Asset Address, Mode
  - Mode: 0 = 4bpp (16-color); 1 = 8bpp (256-color)
- Bytes 2-5: X,Y Coordinates (10 bits, little-endian)
  - X: -63 to 639; Y: -63 to 479
- Byte 6: Collision, Z-level, Flipping
  - Collision Mask: Set bit for each collision “class”
  - Z-level: 0 = off; 1 = behind layers; 2 = between layers; 3 = in front of layers
  - V/H-Flip: Set = Flipping enabled
- Byte 7: Dimensions, Palette Offset
  - Sprite Height/Width: 0 = 8 pixels; 1 = 16 pixels; 2 = 32 pixels; 3 = 64 pixels
  - Palette Offset: 0-15; Sprite color index 0 = Palette color index (16 * offset)
Address (12:5)
Mode	-	-	-	Address (16:13)
Collision Mask	Z-Level	V-Flip	H-Flip
Sprite Height	Sprite Width	Palette Offset

---
Mode 0 Sprites
4bpp (16 colors), 4-bit palette offset
Change offset for different looks
0
16
32
48
Offset 0:
Offset 1:
Offset 2:
Offset 3:

---
Mode 1 Sprites
{
8bpp, full 256-color palette
Twice the VRAM, VERA work units
64x64
{
64x64
Custom Palette

---
Placing a Sprite
Define sprite in RAM, copy to VRAM, place as sprite 1 on screen @ 150,100
VERA_CTRL = $9F25 ldx #10 lda #KON
VERA_BANK = $9F22 @cycle_loop: @wai_off_loop:
VERA_HIGH = $9F21 bit YM_DATA wai
VERA_LOW = $9F20 bmi @cycle_loop dey
VERA_DATA0 = $9F23
VRAM_BALL = $04560 lda #KON bne @wait_off_loop
SPRITE1_ATTR = $1FC08 lda #(ALL_ON | CH2) bne @cycle_loop
ag_ball: sta YM_DATA rts
.byte $00,$69,$95,$00
.byte $05,$8b,$dc,$80
.byte $26,$9e,$ff,$d2
.byte $35,$ad,$ff,$c6
.byte $24,$9c,$ef,$a5
.byte $13,$69,$bb,$81
.byte $01,$35,$77,$40
.byte $00,$12,$21,$00

---
Example Program:
Music Player
Plays first 10 measures of “Eine kleine Nachtmusik”
Wolfgang Amadeus Mozart (K. 525)
“Mario Bros. Theme”
4 piano voices, 4 strings voices
Extra Program: Cavy’s Quest