How to Program in Assembly Language
for the
Lesson 17: FM Synthesis

---
Yamaha YM2151
- Also known as the FM Operator Type-M (OPM)
- 8 stereo voices
- 4-function Frequency Modulation
- Noise generator
- 8 octave range

---
Register Interface
- Wait for Write Ready
  - Read $9FE1
  - Bit 7 clear
- Set register address
  - Write $9FE0
- Set register value
  - Write $9FE1

---
Defining Instruments
- Write “Patch” configuration parameters for channel on each function.
  - Functions: M1, C1, M2, C2
- Set channel control registers
  - Right/Left Channels, Feedback Level
  - Function Connections:

---
Playing Notes
- Key On (KON) Register: $08
  - Bits 6:3 – Functions Enabled (C2, M2, C1, M1)
    - All clear = Key Off
  - Bits 2:0 – Channel Number (0-7)
- Key Code (KC) Register: $28-$2F (per channel)
  - Bits 6:4 – Octave (0-7)
  - Bits 3:0 – Chromatic Note (0-2,4-6,8-10,12-14 → C# to C)
  - $3E = Middle C
- Key Fraction (KF) Register: $30-$37 (per channel)
  - Bits 7:2 – Fraction (0-63 → 0 to 98.4 cents higher)

---
Repeating a Note
Play Middle C on second channel for half second, rest half second, repeat 10 times
YM_REG = $9FE0 ldx #10 ldy #30
YM_DATA = $9FE1 @cycle_loop: @wai_off_loop:
KON = $08 bit YM_DATA wai
ALL_ON = $78 bmi @cycle_loop dey
CH2 = $01 lda #KON bne @wait_off_loop
KC = $28 sta YM_REG dex
MIDDLE_C = $3E lda #(ALL_ON | CH2) bne @cycle_loop
        sta YM_DATA rts
ostinato: ldy #30
   lda #KON @wait_on_loop:
   sta YM_REG wai
   lda #CH2 dey
   sta YM_DATA bne @wait_on_loop
   lda #(KC | CH2) lda #KON
   sta YM_REG sta YM_REG
   lda #MIDDLE_C lda #CH2
   sta YM_DATA sta YM_DATA

---
Noise Generator
- Works through channel 8 (index 7) C2 function slot
  - Play by writing $47 to KON
  - Stop by writing $07 to KON
- Noise Enable / Noise Frequency Register @ $0F
  - Bit 7 – NE (0 = normal FM, 1 = noise)
  - Bits 4:0 – NFRQ (freq = OPM clock freq / (32 * NFRQ))
    - Range: 3.5 kHz (NFRQ = 31) to 111.9 kHz (NFRQ = 1)
- VERA PSG: Better alternative?

---
Example Program:
Music Player
Plays first 10 measures of “Eine kleine Nachtmusik”
Wolfgang Amadeus Mozart (K. 525)
“Mario Bros. Theme”
4 piano voices, 4 strings voices
Extra Program: Cavy’s Quest